DIGITAL VIDEO RECORDER

USER MANUAL

IE Internet browser login address: http://www.e-seenet.com

Catalog

Catalog	1

Preface	4

Catalog	4

Charpter One Product Description	4

1.1 Product Overview	4

1.2 Product Appearance	5

1.3 Technical Parameters	5

1.3.1、51 Series	5

1.3.2、52 Series	7

1.3.3、53 Series	9

1.4 Features	10

Charpter Two Introduction of Product Appearance Structure	11

2.1 Panel Description	11

2.2 Product Interface Description	12

2.3 Mouse Operation Instructions	13

2.4 Remote Control Instructions	13

2.5 Input Method	14

Charpter Three Installation and Connection	14

3.1 Installation Notes	14

3.1.1 Check the Goods	14

3.1.2 Regarding front panel and rear panel	14

3.2 Hard disk installation	14

Charpter Four Instruction of operating system	16

4.1 Power on/login/login out/restart/turn off screen output/ power off	16

4.1.1 Power on	16

4.1.2 login	16

4.1.3 login out	17

4.1.4 restart	17

4.1.5 turn off screen output	17

4.1.6 power off	17

4.2 Preview	17

4.3 Boot wizard	17

4.4 Connect analog camera and add IPC camera	20

4.5 screen wheel tour	22

4.6 electronic enlarge	22

4.7 Basic operation instructions	22

4.7.1 Enter menu mode	22

4.7.2 Menu composition description	23

4.7.3 Exit menu mode	23

4.8 Main menu	23

4.9 Video playback	24

4.9.1 Video search	24

4.9.2 Playback tool	25

4.10 Video backup	25

4.11 Color adjustment	26

4.12 Channel mode	26

4.13 PTZ control	27

4.13.1 PTZ Regulation	27

4.13.2 Call preset	27

4.13.3 Call the cruise line	28

4.14 Recording function	29

4.14.1 Manual video record	29

4.14.2 Timer video record	29

4.14.3 Mobile video record	30

4.14.4 Alarm video record	31

4.15 System settings	31

4.15.1.1General setting	32

4.15.1.2 Time setting	32

4.15.1.3Hard disk setting	33

4.15.1.4 Screen setting	33

4.15.2 Channel setting	34

4.15.2.1 Encoding setting	34

4.15.2.2 PTZ setting	35

4.15.2.3 Channel OSD	36

4.15.2.4 Code stream value	36

4.15.3 Video setting	37

4.15.3.1 Video recording plan	37

4.15.3.2 Video detection	37

4.15.3.3 Alarm setting	39

4.15.4 Network setting	40

4.15.4.1 Network setting	40

4.15.4.2 Dynamic domain name	41

4.15.4.3 FTP	42

4.15.4.3 FTP	42

4.15.4.4 PPPoE	42

4.15.4.4 PPPoE	42

4.15.4.5 3G	43

4.15.4.5 3G	43

4.15.4.6 E-Mail	43

4.15.4.6 E-Mail	43

4.15.5 System management	44

4.15.5.1 Version information	44

4.15.5.2 Hard disk information	44

4.15.5.3 Log information	45

4.15.5.4 User management	45

4.15.5.5 System maintenance	46

4.15.5.6 Software upgrade	46

4.15.5.6 Original setting	47

Charpter Five Local area network access	47

5.1 Login	47

5.2 Preview	49

5.3 Playback	49

5.4 Configuration	50

Charpter Six Access of eseenet	50

6.1 Login by eseenet ID	50

6.2 Login by user name	51

6.3 Playback	52

Charpter Seven Mobile phone terminal	53

7.1 Introduction	53

7.2 Login	53

7.2.1、Install	53

7.2.2、Run the software	53

7.2.3、Add equipment	54

7.2.4、Preview	55

7.2.5、Remote playback	56

7.2.6、Snapshot / video / picture quality	57

7.2.7、Alarm by mobile phone APP	57

Charpter Eight Appendix	58

8.1 Conversion of hard disk capacity unit	58

8.2 Video required capacity calculation	58

preface

Statement

- We did our best to promise the integrity and accuracy of the content, but also inevitably there is technically inaccuracy, points not matching with product function and operation or typographical errors. If any doubt or dispute, please refer to the final interpretation of Juan.

- The products and manuals will be updated in real time without notice.

- The contents of this manual is to provide reference for the user only, and is not guaranteed to be consistent with the physical.  Please refer to the real product.

- The mentioned parts, components and accessories are only for instruction use. It does not mean that the purchase model have these in configuration. Configuration in detail please refer to the packing list.

important clause

When using the video monitoring equipment, the use and maintenance of the monitoring interface, please strictly comply with applicable laws and regulations. For the use of video surveillance equipment which is used to the privacy of others illegal purpose, belongs to illegal eavesdropping.

Regarding default

- the original super administrator account: admin.

- the default password: null

- The equipment default automatically obtain IPv4 address: 192.168.1.114

In order to guarantee the security of your information, we suggest you to modify the original password to a high strength one after the first time login. Please take care of your user name and password

- The hard disk defaults automatic coverage

- The routine setting defaults boot wizard.

Catalog

Chapter 1 Product description

1.1 Product Overview

This device is a digital monitoring product designed for the field of security. It adopts the embedded processor and embedded operating system, combined with the latest technology in the IT field, such as video and audio compression / decompression, large capacity hard disk recording, TCP / IP network technology, solidified code in flash, making system more stable. This device have features of DVR and DVS. It can work independently or connect with other device to make a strong security surveillance network which can be used in banking, telecommunications, electricity, justice, transportation, residential, factories, warehouses, water conservancy facilities, and other fields.

1.2 product appearance

1.3 technical specification

### 1.3.1、51 Series

| Specification/Model | R5104-H | R5108-H | R5116-H |
| --- | --- | --- | --- |
| Audio and Video | Video output | BNC/VGA/HDMIoutput |
|  | Audio input | support |
|  | Audio input | support |
|  | Video compression standard | H.264 |
|  | Video standard | PAL、NTSC |
|  | Coding resolution | 1080P/720P/960H/D1 |
|  | Preview resolution | TVI 2.0（720P@25/30/50/60fps，half-1080P@25/30fps），AHD（720P@25/30fps，half-1080P@25/30fps），CVBS（960H@PAL/NTSC） |
|  | Encoding frame rate | 1080P-H(960x1080）/720P@16fps; 960H/D1@25fps | 1080P-H(960x1080)/720P@16fps; 960H/D1@25fps | 1080P-H(960x1080)/720P@12fps; 960H@20fps; D1@25fps |
|  | Audio compression standard | G711 |
| Storage | Hard disk type | SATA |
|  | Hard disk interface | 1*SATA | 2*SATA | 2*SATA |
|  | USB Backup | Support |
| Recording management | Recording type | manual recording / timing recording/ motion detection recording / alarm recording |
|  | Recording mode | loop cover / stop video |
|  | Local playback | 4 channel playback | 4 channel playback | 4 channel playback |
|  | Playback control | pause / play Fast forward (X2 X4 X8) |
|  | Searching mode | Channel number / video type / date (separate or combined query) |
| network management | Ethernet | 10M/100M adaptive network |
|  | Maximum channel number | 4 channel | 8 channel | 16 channel |
|  | Supported protocol | TCP/IP，DHCP，UDP，SMTP，FTP,PPPOE,NTP,RTMP,RTSP |
|  | Connected protocol | ONVIF，N1 ONVIF，N1 |
|  | Client monitoring | Support CMS client, web monitoring, mobile phone monitoring |
| External interface | Network interface | RJ45 10M/100M adaptive Ethernet port | RJ45 10M/100M adaptive Ethernet port |
|  | USB interface | 2*USB2.0 |
|  | PTZ interface | Support RS485 interface |
|  | UTC protocol | Support |
|  | Control device | mouse |
|  | Remote control | Support |
|  | Alarm input | Support |
|  | Alarm output | Support |
| Smart phone | Operating system | Android/IOS |
|  | Protocol supported | TCP/UDP/ |
| Features | picture layout | 4 channel | 8 channel | 16 channel |
|  | Alarm notification mode | alarm / buzzer / message alarm / mobile phone APP alarm |
|  | Electronic enlarge | Support |
|  | Region occlusion | Not support |
|  | Video loss alarm | Support |
|  | Video occlusion alarm | Not support |
| General characteristics | Working temperature | -10℃～+55℃ |
|  | Working humidity | 10%～90% |
|  | Power | DC12V |
|  | Power | ≦15W（excluding hard disk） |
|  | Language | English / Chinese / Korean / Japanese / Arabic / Persian / Hebrew / Spanish / Hungarian / Russian / French / German / Thai / Vietnamese / Turkish / Italian / Danish |

| Specification/Model | R5124-H | R5132-H |
| --- | --- | --- |
| Audio and Video | Video output | BNC/VGA/HDMI output |
|  | Audio input | support |
|  | Audio input | support |
|  | Video compression standard | H.264 |
|  | Video standard | PAL、NTSC |
|  | Coding resolution | 1080P/720P/960H/D1 |
|  | Preview resolution | TVI 2.0（720P@25/30/50/60fps，half-1080P@25/30fps），AHD（720P@25/30fps，half-1080P@25/30fps），CVBS（960H@PAL/NTSC） |
|  | Encoding frame rate | 1080P-H(960x1080)/720P@15fps; 960H@20fps; D1@25fps | 1080P-H(960x1080)/720P@15fps; 960H@20fps; D1@25fps |
|  | Audio compression standard | G711 |
| Storage | Hard disk type | SATA |
|  | Hard disk interface | 2*SATA | 2*SATA |
|  | USB Backup | Support |
| Recording management | Recording type | manual recording / timing recording/ motion detection recording / alarm recording |
|  | Recording mode | loop cover / stop video |
|  | Local playback | 4 channel playback | 4 channel playback |
|  | Playback control | pause / play Fast forward (X2 X4 X8) |
|  | Searching mode | Channel number / video type / date (separate or combined query) |
| network management | Ethernet | 10M/100M adaptive network |
|  | Maximum channel number | 24 channel | 32 channel |
|  | Supported protocol | TCP/IP，DHCP，UDP，SMTP，FTP,PPPOE,NTP,RTMP,RTSP |
|  | Connected protocol | ONVIF，N1 |
|  | Client monitoring | Support CMS client, web monitoring, mobile phone monitoring |
| External interface | Network interface | RJ45 10M/100M adaptive Ethernet port |
|  | USB接口 USB interface | 2*USB2.0 |
|  | PTZ interface | Support RS485 interface |
|  | UTC protocol | Support |
|  | Control device | mouse |
|  | Remote control | Support |
|  | Alarm input | Support |
|  | Alarm output | Support |
| Smart phone | Operating system | Android/IOS |
|  | Protocol supported | TCP/UDP/ |
| Features | picture layout | 24 channel | 32 channel |
|  | Alarm notification mode | alarm / buzzer / message alarm / mobile phone APP alarm |
|  | Electronic enlarge | Support |
|  | Region occlusion | Not support |
|  | Video loss alarm | Support |
|  | Video occlusion alarm | Not support |
| General characteristics | Working temperature | -10℃～+55℃ |
|  | Working humidity | 10%～90% |
|  | Power | DC12V |
|  | Power | ≦15W（excluding hard disk） |
|  | Language | English / Chinese / Korean / Japanese / Arabic / Persian / Hebrew / Spanish / Hungarian / Russian / French / German / Thai / Vietnamese / Turkish / Italian / Danish |

### 1.3.2、52 Series

| Specification/Model | R5204-H | R5208-H | R5216-H |
| --- | --- | --- | --- |
| Audio and Video | Video output | BNC/VGA/HDMIoutput |
|  | Audio input | support |
|  | Audio input | support |
|  | Video compression standard | H.264 |
|  | Video standard | PAL、NTSC |
|  | Coding resolution | 1080P/720P/960H/D1 |
|  | Preview resolution | TVI 2.0（720P@25/30/50/60fps，1080P@25/30fps），AHD（720P@25/30fps，1080P@25/30fps），CVBS（960H@PAL/NTSC） |
|  | Encoding frame rate | 1080P@15fps 1080P-H(960x1080)/720P/960H/D1@25fps; | 1080P@12fps 1080P-H(960x1080)/720P@20fps; 960H/D1@25fps | 1080P@15fps 1080P-H(960x1080)/720P/960H/D1@25fps; |
|  | Audio compression standard | G711 |
| Storage | Hard disk type | SATA |
|  | Hard disk interface | 1*SATA | 2*SATA | 2*SATA |
|  | USB Backup | Support |
| Recording management | Recording type | manual recording / timing recording/ motion detection recording / alarm recording |
|  | Recording mode | loop cover / stop video |
|  | Local playback | 4 channel playback | 4 channel playback | 4 channel playback |
|  | Playback control | pause / play Fast forward (X2 X4 X8) |
|  | Searching mode | Channel number / video type / date (separate or combined query) |
| network management | 以太网 Ethernet | 10M/100M adaptive network |
|  | Maximum channel number | 4 channel | 8 channel | 16 channel |
|  | Supported protocol | TCP/IP，DHCP，UDP，SMTP，FTP,PPPOE,NTP,RTMP,RTSP |
|  | Connected protocol | ONVIF，N1 |
|  | Client monitoring | Support CMS client, web monitoring, mobile phone monitoring |
| External interface | Network interface | RJ45 10M/100M adaptive Ethernet port | RJ45 10M/100M/1000M adaptive Ethernet port |
|  | USB interface | 2*USB2.0 |
|  | PTZ interface | Support RS485 interface |
|  | UTC protocol | Support |
|  | Control device | mouse |
|  | Remote control | Support |
|  | Alarm input | Support |
|  | Alarm output | Support |
| Smart phone | Operating system | Android/IOS |
|  | Protocol supported | TCP/UDP/ |
| Features | picture layout | 4 channel | 8 channel | 16 channel |
|  | Alarm notification mode | alarm / buzzer / message alarm / mobile phone APP alarm |
|  | Electronic enlarge | Support |
|  | Region occlusion | Not support |
|  | Video loss alarm | Support |
|  | Video occlusion alarm | Not support |
| General characteristics | Working temperature | -10℃～+55℃ |
|  | Working humidity | 10%～90% |
|  | Power | DC12V |
|  | Power | ≦15W（excluding hard disk） |
|  | Language | English / Chinese / Korean / Japanese / Arabic / Persian / Hebrew / Spanish / Hungarian / Russian / French / German / Thai / Vietnamese / Turkish / Italian / Danish |

### 1.3.3、53 Series

| Specification/Model | R5304-H |
| --- | --- |
| Audio and Video | Video output | BNC/VGA/HDMI output |
|  | Audio input | support |
|  | Audio input | support |
|  | Video compression standard | H.264 |
|  | Video standard | PAL、NTSC |
|  | Coding resolution | 1080P/720P/960H/D1 |
|  | Preview resolution | TVI 2.0（720P@25/30/50/60fps，1080P@25/30fps），AHD（720P@25/30fps，1080P@25/30fps），CVBS（960H@PAL/NTSC） |
|  | Encoding frame rate | 1080P/720P/960H/D1@25fps |
|  | Audio compression standard | G711 |
| Storage | Hard disk type | SATA |
|  | Hard disk interface | 2*SATA |
|  | USB Backup | Support |
| Recording management | Recording type | manual recording / timing recording/ motion detection recording / alarm recording |
|  | Recording mode | loop cover / stop video |
|  | Local playback | 4 channel playback |
|  | Playback control | pause / play Fast forward (X2 X4 X8) |
|  | Searching mode | Channel number / video type / date (separate or combined query) |
| network management | Ethernet | 10M/100M adaptive network |
|  | Maximum channel number | 4 channel |
|  | Supported protocol | TCP/IP，DHCP，UDP，SMTP，FTP,PPPOE,NTP,RTMP,RTSP |
|  | Connected protocol | ONVIF，N1 |
|  | Client monitoring | Support CMS client, web monitoring, mobile phone monitoring |
| External interface | Network interface | RJ45 10M/100M adaptive Ethernet port |
|  | USB interface | 2*USB2.0 |
|  | PTZ interface | Support RS485 interface |
|  | UTC protocol | Support |
|  | Control device | mouse |
|  | Remote control | Support |
|  | Alarm input | Support |
|  | Alarm output | 支持 Support |
| Smart phone | Operating system | Android/IOS |
|  | Protocol supported | TCP/UDP/ |
| Features | picture layout | 4 channel |
|  | Alarm notification mode | alarm / buzzer / message alarm / mobile phone APP alarm |
|  | Electronic enlarge | Support |
|  | Region occlusion | Support |
|  | Video loss alarm | Support |
|  | Video occlusion alarm | Support |
| General characteristics | Working temperature | -10℃～+55℃ |
|  | Working humidity | 10%～90% |
|  | Power | DC12V |
|  | Power | ≦15W（excluding hard disk） |
|  | Language | English / Chinese / Korean / Japanese / Arabic / Persian / Hebrew / Spanish / Hungarian / Russian / French / German / Thai / Vietnamese / Turkish / Italian / Danish |

## 1.4 Functional characteristics

- The real-time monitoring

- Support VGA/HDMI/CVBS output at the same time

- Support real-time video preview of 1/4/6/8/9/16/24/32 channel

- Support electronic enlarge

- Support the channel name changing

- Support the switch of analog cameras and high-definition camera

- Compressed storage

- Adopting H.264 video compression technology which has lower compression ratio and better image quality

- Support video stream / composite video stream

- Support video files and logs query

- Support USB backup

- Support network backup

- Support the 4TB hard disk. Recycling / automatic stop is optional for hard disk

- Video playback

- Support manual recording, time recording, motion detection recording, alarm recording

- Support query recording and all day long / hour query recording distribution

- Alarm function

- Support picture detection alarm. Each picture can be provided with a plurality of separate inspection area

- Support alarm by external alarm box

- Support mobile alarm

- Support video loss alarm

- Support alarm in the fixed time

- Support video occlusion alarm

- Support message alarm

- Support buzzer alarm

- Support mobile phone APP alarm

- PTZ function

- A variety of control protocol

- Support 255 preset positions and the cruise line

- Support remote monitoring

- Support built-in menu and command interchange

- Network function

- Use eseenet to monitor by network and no need any complicated set up.

- Support TCP/IP, DHCP, PPPoE protocol

- Support sub stream. QCIF/CIF/D1 resolution is optional

- Support static setup of IP/DHCP to automatically obtain /3G card dial

- For remote monitoring, we have CMS and http://www.e-seenet.com and eseecloud app for optional

- Support real-time remote monitoring / remote PTZ control / remote host configuration adjustment

- Support the CMS platform which can manage multiple devices at same time

- Support remote playback / remote download of video record

- Other functions

- Support the boot wizard and quick settings

- Support USB mouse and remote control

- Support software upgrade: upgrade by U disk

- Support switch of multi languages

Chapter 2 Introduction of product appearance and structure

2.1 Panel description

4 channel front panel introduction:

| Serial number | Name | Function descriptions | Serial number | Name | Function descriptions |
| --- | --- | --- | --- | --- | --- |
| 1 | PWR | Power indicator | 8 | REC | REC key |
| 2 | CH1~CH4 | Switch for single channel | 9 | PTZ | PTZ control key |
| 3 | QUAD | Multi screen key | 10 | ESC | Exit key |
| 4 | HDD | Hard drive indicator light | 11 | MENU | Menu key |
| 5 |  | Status light | 12 | ▲▼ | Direction key |
| 6 | FN | Reserved key | 13 |  | Confirm key |
| 7 | PLAY | Record playback key | 14 |  |  |

8 channel front panel introductions:

| Serial number | Name | Function descriptions | Serial number | Name | Function descriptions |
| --- | --- | --- | --- | --- | --- |
| 1 | HDD | Hard drive indicator light | 8 | PLAY | Record playback key |
| 2 |  | Status light | 9 | ESC | Exit key |
| 3 | CH1~CH8 | Switch for single channel | 10 | MENU | Menu key |
| 4 | PW | Power indicator light | 11 | ▲▼ | Direction key |
| 5 | IR | Infrared receiver | 12 |  | Confirm key |
| 6 | QUAD | Multi screen key |  |  |  |
| 7 | REC | REC key |  |  |  |

2.2  Product interface introduction

4 channel rear panel introduction

| Serial number | Name | Function descriptions | Serial number | Name | Function descriptions |
| --- | --- | --- | --- | --- | --- |
| 1 | VIDEO IN | Video input interface | 8 | VGA | Video output interface (which can be used to connect the output interface of the computer display screen) |
| 2 | AUDIO OUT | output interface | 9 | NET | RJ-45 standard network interface |
| 3 | VIDEO OUT | Video output interface | 10 | USB | Standard USB interface |
| 4 | AUDIO IN | Audio input interface | 11 | RS485 | To connect Rs-485 control lines |
| 5 | AUDIO IN | Audio input interface (Extended) | 12 | DC12V | 12V power interface |
| 6 | Alarm | Alarm input interface | 13 | fan | Cooling fan with temperature control |
| 7 | POWER | Power switch |  |  |  |

8 channel rear panel introduction

| Serial number | Name | Function descriptions | Serial number | Name | Function descriptions |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-8 | Video input interface | 8 | NET | RJ-45 standard network interface |
| 2 | VIDEO OUT | Video output interface | 9 | USB | Standard USB interface |
| 3 | AUDIO OUT | Audio output interface | 10 | RS-485 | RS-485 interface |
| 4 | AUDIO IN | Audio input interface | 11 | DC12 | 12V power interface |
| 5 | Alarm | Alarm input interface | 12 | AUDIO IN 3-8 | Audio input interface (3-8) extension |
| 6 | POWER | Power switch | 13 | fan | Cooling fan with temperature control |
| 7 | VGA | Video output interface (which can be used to connect the output interface of the computer display screen) |  |  |  |

2.3 Mouse operation instructions

| Mouse key | Operation | Function | Examples |
| --- | --- | --- | --- |
| Left key | One click | Select target | 1. Select the preview window, playback window 2. Select the button, edit box, drop-down box, check box |
|  | Double click | Window zoom | 1. Switch between single screen and multi screen during previewing. 2. Switch between single screen and multi screen during playback. |
|  | Drag | Area setting | Set area for mobile detection |
| Middle key | Rolling | Change content | 1. Change the value of the [Channel] edit box 2. Change the contents of the [time] edit box |
| Right key | One click | Close interface | 1. Right click to close the operating interface |

## 2.4 Remote controller instruction

| Name | Funtion |
| --- | --- |
| POWER | Turn off the screen output |
| DEV | Device key: first press the DEV key, then press the number key to enter the device number which is the same with the host device. Press the "ENTER" key to save the settings. The control is effective. |
| 0-9 | Number keys |
| MENU | Menu key; Clear the entire area while setting the motion detection area. |
| ESC | Exit key |
| ▲ | In the menu state, choose upward; In PTZ mode, control the dome to rotate upward. |
| ▼ | In the menu state, choose downward; In PTZ mode, control the dome to rotate downward. |
|  | In the menu state, choose left side; In PTZ mode, control the dome to rotate to left side. |
|  | In the menu state, choose right side; In PTZ mode, control the dome to rotate to right side. |
| ENTER | Confirm key |
| PLAY | Record playback key |
| FN | Auxiliary key |
| REC | Recording key |
| VIEW | Multi screen key |

Instruction

- If there are multiple devices in the same place, remote controller will first choose a device according to the equipment number. So you should define a unique device number for each piece of equipment, or remote controller may operate multiple devices with the same device number at the same time.

2.5 Input method instruction

| Name | Key description | Function description |
| --- | --- | --- |
| Number | 0～9 | Enter the number 0 ~ 9 |
| Symbol | ~ ！@ # % $^&*( ) - =，。；、/ \ [ ] | Input symbol |
| English | a～z | Input lowercase letters a to Z |
| Capital/lowercase | caps | Switch of capital and lowercase |
| Backspace | <- | Delete a character before the cursor |
| All clear | clr | Delete all contents |
| Space |  | Space key |
| TAB key | TAB key | Tabulator |

Instruction

- When it can only enter numbers, input method interface will appear on the right side.

Chapter 3 Installation and connection

3.1 Installation notes

3.1.1 Check goods

1. Please check whether the packing of the equipment is damaged obviously. Product packaging is made of protective materials which can cope with most of the accidents in the transportation process;

2. Please take out the equipment, remove the plastic protective film of hard disk recorder and check whether there is obvious damaging marks;

3. Open the case and check if there is any loose on the front panel data lines, power lines, connection between fan power and the motherboard;

4. please note that the power supply could not exceed the normal operating voltage range.

3.1.2 About front panel and rear panel

1, There are detailed descriptions for all the functions of keys in the front panel and the various interfaces in the rear panel;

2, Please carefully check the model number in front panel film to see whether it is consistent with the one you ordered. The label in rear panel is very important for our company's after-sales service. Please protect it well.

3.2 Install the hard disk

Please install the hard disk when you use it for first time.      ( This picture needs to be changed. )

3.3 Peripheral connection

| NO | Hardware name | NO | Hardware name |
| --- | --- | --- | --- |
| 1 | displayer | 9 | Network cable |
| 2 | VGA wire | 10 | Audio output device |
| 3 | monitor | 11 | Audio input/output wire |
| 4 | Video input/output wire | 12 | Audio input device |
| 5 | Power plug | 13 | mouse |
| 6 | Power adapter | 14 | HDMI wire |
| 7 | Analog camera | 15 | LCD (liquid crystal display) |
| 8 | switch |  |  |

Chapter 4   Operation System Declaration

## 4.1Boot / Login / Logout / Restart / Shutdown screen output / Shut down

### 4.1.1 Boot

Remark:



1, Check the access voltage and DVR to match the requirements and ensure the DVR GND correctly .

2, Power supply is not normal, it will cause the DVR does not work properly, or even damage to the DVR , recommend using regulated power supply.

Specific Booting procedures:

1, Plug in the power , front-panel power indicator is red ;

2, Open the boot panel power switch , the device started, as shown below :

Description:

● For audio output, before turning , you can access an audio output device

● If the host is powered , the device not equipped with a hard disk , or install the hard disk when the boot is not detected , after starting the video preview screen will display a hard disk is not hard to find in a dialogue box .

### 4.1.2  Login

When the system is turned on and started after waiting for system initialization , the system will automatically pop up the login screen . As shown below. After user complete login to continue.

Operation Procedure:

1 , Left-click on the user name edit box and enter the user name logged on the machine , the user's defaulted factory setups named admin.

2 , Left-click the Password box and enter the machine login password, if the defaulted factory setups is empty , that is not filled .

3 , Left-click "OK " to complete the login

Description:

- password can be numbers, characters , operators, and points , *, # number, for no longer than 10 characters.

### 4.1.3 Logout

User log off in process , right choose shortcut menu, choose Exit System, click the user logs off to complete. As shown below.

If users need to log out automatically in System Setup - > General Setup, automatically logged out will be is set to ON. The system will automatically log off the system within one minute without an operation, when the operation again, need to re- enter your user name and password.

### 4.1.4  Restart

If user need to restart the machine in process, right choose shortcut menu, choose Exit system , click the system restart to complete.

### 4.1.5 Shutdown screen output

If user needs to close the output screen in process, right choose shortcut menu, choose Exit system , click Close to complete the screen output.

### 4.1.6 Shut down

If user needs to turn off the system, right choose shortcut menu, choose Exit system , click Close to complete the system .

## 4.2 Preview

The device enters preview screen after starting. In the preview screen you can see system date, time and channel name. Press the corresponding number key panel or click the left mouse button , you can single-screen preview ; press the panel "QUAD" key or click the left mouse button , you can return to the multi-screen preview mode .

4.3 Boot Wizard

System will automatically open the "Setup Wizard " interface guides after login, to lead user to the basic setups so that the unit is working properly .

setup first : Setup Wizard. If setup Wizard is displayed while the next boot. Client is download through scanning the two-dimensional code  which support Android and Apple systems currently. They are described in FIG. Click the "Next" button after setup.

setup second: General setups. Can time zone, the system time , time synchronization , date format, language selection, video format , key type , the remote control number be set , as shown below , click "Next" button after setup completion;

setup Three: a key to the Internet.

1, Into the a key to the internet system will be intranet diagnosis , if internet errors prompted , click auto-configuration or manually configure for the network configuration. The system is automatically configured to obtain an IP address , automatic networking , as shown below ;

2, If the auto-configuration problem persists , check that the current Internet access methods . If PPPOE access, clickable manual configuration , enter PPPOE setups , check on, enter your user name and password , click OK ;

3, After setup the access, the system will be re-tested online status . If this does not normally networking, Please operate according to the network status prompts. If no need networking , click the "Next" button ;

setup Four: Channel Mode. Set analog channel and digital channel number , and set automatic mode and AHD mode . If the defaulted auto mode , the camera automatically recognizes analog access , click the Next button to complete the setup of this item . For hybrid access high-definition analog cameras and IPC, pull the slider and the selected point is determined before the VCR restarting. Click Add IP cameras , video management interface that is entered , you can add IPC cameras. Specific methods can refer to 4.4.

setup Five: encoding setups. Operation such like the main stream, the secondary stream and coding mode can be set, to achieve a key to copy all channels , which as shown below

setup Six: Drive setups. can display all hard disks about this DVR, and do hard disk formatted , which is shown below, click "Next" button after setup completion ;

Description

● If you do not start the boot wizard, please click right mouse button - > System Setup - > General Setup to cancel Boot Wizard checked checkbox

4.4 Access analog cameras and IP Camera added

Operation Procedure:

First, access to analog camera . Ensure proper access analog camera , if it can not display images correctly , perform the following actions:

1, Right Main Menu " Channel mode " to enter the setup interface , as shown below :

2, The system defaulted is automatic mode, automatic identification of high-definition analog camera access , if the camera does not recognize AHD Camera, please check AHD mode.

Second, add the IPC.

1, IPC and the video recorder must be connected to a switch belong to the same network through Ethernet port ;

2, Into the channel mode , pull the slider between analog channels and digital channels, for example of 8 channel, if you need access to five analog cameras and three IPC, then pull the slider , and if click OK after adjustment, restarting will be prompted.

3, Log into the channel mode after restarting, click Add IP cameras into the video management interface , as shown below ( or right main menu, select Video Manager to enter the video interface ) , imitate this for other channels. Click the refresh that IPC camera can be found, select the camera, click the Add ( or double-click the selected IPC camera ) , then added to the corresponding channel, as shown below:

Details Menu

| Function | Description | Remark |
| --- | --- | --- |
| Update | Search IPC |  |
| Add one | Add single IPC |  |
| Auto Add | A button add a searched IPC | Click on this function , the choice automatically modify IP address , otherwise if the election, IP address will not be modified. |
| Delete Channel | Delete a selected channel |  |
| Delete all | Delete all the added channel |  |
| Edit Channel | edit added IPC connection parameter in channel | Editable protocol, IP address, port, user name, password, etc. |
| Channel setups | The IPC specific parameters channel set | Specific reference 4.15.2.1 encoding setups |
| The remaining network bandwidth | Displays the network connection bandwidth | The total bandwidth can not exceed the remaining bandwidth is displayed here , if it is a negative value should be adjusted main stream |

Remark

● Channel mode is defaulted to auto mode, automatically recognizes analog access, if access can not display AHD, it needs to enter channel mode check AHD mode ; the system is defaulted to access analog cameras , video manager menu is not displayed in the the main menu, only after adjustment of the number of channels of digital video recorders, video manager menu will appear after restarting, you can enter the video management interface to add IPC

● If you select a digital channel , the IP camera will be added to the last channel

● IPC connection can be mixed with conventional analog and HD analog AHD and TVI, currently supporting every two docking mode, that channel 1-2 to be AHD, TVI or ordinary analog meanwhile, if access different cameras,only show one camera

● IPC supports 1080P

4.5  Screen polling

Operation Procedure:

1, Right Main Menu " System Setup" - > " General Setup " -> " Screen Setup " to enter the interface, as shown below :

2, Set the polling time , respectively, 2,3,4,5,8,10 seconds

3, After setup, check the " automatic switch" is turned on, the mouse click ok

Description

● " Auto switch " on automatic polling, select the screen switching time, the interface will start switching channel page at the set time, there are two kinds of screen 1,4 switching mode

● " Auto switch " such as checking the "Skip Video Loss " If there are no channels displayed on the screen , the channel screen polling will automatically skip this screen

4.6 Electronic zoom

Operation Procedure:

1, Double-click any video channel on the main interface, you can use an electronic zoom mode

2, Hold down the left mouse button to zoom in or out part of the area of the image

3, Double-click the left mouse button or middle mouse button to exit screen electronic amplification

Description

● Double-click to enter video channel interface, to electronic amplification image

## 4.7Menu Basic Operations

4.7.1Enter the menu mode

[Main Menu / MENU ] button to access the device main menu . [Playback / PLAY ] button to enter the playback interface .

【Video / REC 】 shortcut keys, enter manually recording interface. [PTZ / PTZ ] button to enter the PTZ control interface .

Description

● The defaulted password is blank, just click the OK button to enter the menu.

4.7.2 Menu Composition Description

Menu component units mainly as the following:

(1) Check box: provide two kinds of state selection , "√" indicates effective , "□”" means invalid , use keys 【↑】【↓】【←】【→】to move, [OK / ] key or click the left mouse button to select.

For example: in the menu page of video search , the "channel" and " record mode " check box.

(2) Selection box : Depending on the options contents of the system drop-down box , select the target content. Use key【↑】【↓】【←】【→】or click the left mouse button to select.

For example: within the menu page of encoding setups, the "channel" and "stream type" check box.

(3) List box : display the search result in the list , you can choose one of the corresponding operation in the list provided .

For example : press the video backup results list to click【ok / 】 key or the left mouse button to select the file.

(4) Edit box: through the edit box , enter the name of the target .

For example: display menu setup page, "Channel Title" edit box, you can enter numbers, letters , punctuation, and so on.

a) through the panel 【↑】【↓】【←】【→】 keys or the mouse to move the cursor positioning edit box , press 【】key or click the left mouse button, then an input keyboard appears, the arrow keys or mouse click button to select the target character to be entered .

b)  Select to click 【OK】【Cancel】 on the keyboard after input completion, or press【ESC】key to save or exit edit mode.

(5) Button: used to perform a specific function or enter the next menu , confirm 【OK/】key and the left mouse button to enter.

4.7.3 Exit menu mode

Press【MENU,【Exit/ESC】or the right mouse button to exit the menu mode.

4.8 Main menu Introduction

Press the MENU button or the right mouse button to popup the main menu , the main menu consists of the following three parts:

Description

● In the menu bar, select the corresponding screen preview mode;

● In the menu bar, respectively: Split Screen, system Setup, Video playback, Video backup, Color adjust, Channel Mode , Video Management, PTZ control , Manual record, Volume, Setup wizard, Exit system can directly enter the corresponding menu page ;

● After entering System Setup,it contains General setup, Channel setup, Record setup, Network setup, System admin.

4.9 Video playback

Operation Procedure:

1, Right click the "Video Playback" - > " manual search " to enter file search interface , as shown below:

2, Choose the required channel playback and video playback mode , click on the "search", which playback time period can be displayed;

3, Click on the " Video Playback " button or click an arbitrary position on the color of the box section

Description

● Click on the video playback , the front three options: 5 minutes, 10 minutes, 30 minutes playback before the current time of 5 minutes, 10 minutes and 30 minutes of video

● Click the "manual search" to choose past time to start playback and video playback time

● Timing color bar :  move color bar as follows:  Alarm color :

4.9.1  Video Search

Select channel: Select target channel you want to search , click the check box to select it.

Video Mode: Select record mode you want to search, click the check box to select it.

Date and Time: In the edit box enter the start and end times for recording to be searched.

Search button : After setup the above search criteria, click the button, the system begins to search for the corresponding video information, and lists the search results, "Red " indicates timing record, "Green" indicates motion detection record, " yellow " means alarm record

Video playback: Playback screen to enter the search interface, search results list box , through the up, down, left , right , or move the mouse positioning period ,【】 key or click the left mouse button on the " Playback " to enter the playback interface .

Cancel button: return to the previous menu.

4.9.2  Playback tool

| Icon | Function | Icon | Function |
| --- | --- | --- | --- |
|  | Hide the playback control interface |  | Pause playback |
|  | Stop playback and exit the playback interface |  | Continue video playback |
|  | Video fast forward multiples |  | Forward |
|  | Backward |  |  |

Description

● Mouse click shrink button to shrink playback control interface, the need to move the mouse to achieve hide

● Display playback control interface , you can right

● There are multiple video fast-forward * 2 / * 4 / * 8 three kinds

● Back, forward buttons are generally backward / forward 10 seconds

4.10 Video Backup

：

Operation Procedure:

1, Right- click on the " Video Backup" , as shown below:

2, Check the mouse channel needs to be backed up , should backup all channels , directly check the " All"

3,The mouse needs to check backup record mode, / manual / time / move / alarm, system all types of video defaulted

4, Modify the start time that is required to backup video files , click "search"

5, After the retrieval is completed , you can check the file needs to back up. Once if  progress bar "Video Backup" to be 100%, suggesting that the backup was successful.

Description

● To ensure USB enough space, otherwise it will cause the backup to fail

● Need to check the backup files to be backed up

● Backup with USB mobile device must be fat32 format

4.11 Color Adjustment

Operation Procedure:

1, Mouse click to drag the control channel, can adjust to hue, brightness, saturation and contrast,

2, Adjust three states: Default , bright , soft, as shown:

Description

● setup a channel parameter is completed, can be set via a button " Copy to " all channels

● If only one channel is set , double-click into the channel, right mouse click to select "Channel adjustment ". Click "Channel adjustment" is defaulted into the first passage

4.12 Channel mode

Operation Procedure:

1, Right- click on the " Channel mode " , as shown below:

2, Pull the slider to adjust the analog and digital channels , then adjust click OK , you are prompted to restart.

Description

● When the system can not automatically obtain input format , through the " Channel mode" manually setup

● If the access of ordinary analog camera and TVI camera, the system will automatically recognize the camera, if properly if TVI doesn’t appear, please confirm whether the TVI2.0 standards, the current system does not support TVI1.0 standards.

● If the access is AHD HD camera , check AHD mode

4.13 PTZ control

4.13.1 PTZ adjustment

Operation Procedure:

1, Right-click the shortcut menu bar " PTZ " to enter its control interface , as shown:

2, Adjustable PTZ direction , click the " Up  / Down  / Left  / Right" arrow keys

3, Click the " zoom/focus/iris " to adjust image brightness, focus, image scaling

Description

● If only one channel is set , double-click into the channel, right mouse click to select " PTZ ". Click " PTZ Control" is defaulted to enter the first channel

4.13.2 To call a preset

Operation Procedure:

1, Right- click into the "System Setup" - > "Channel Setup" - > " PTZ Setup" :

2, Click " ? " to enter the following figure:

3, Click " Up /Down / Left / Right" arrow keys to adjust the PTZ preset position, right mouse click to back to the original interface after adjustment;

4, Click "Go to", the position of the head to start moving just set.

Description

● " Go to " can call any one of the presets, see the preset case

● If you want to cancel PTZ preset position just adjusted, click " Clear " button

4.13.3 Call the cruise line

Operation Procedure:

1, Right- click into the "System Setup" - > "Channel Setup" - > "PTZ Setup"

2, Channel, protocol, baud rate and other parameters can be adjusted;

3, After the adjustment, click " ? " to enter the following figure;

4, Click the " Up / Down  / Left / Right" arrow keys to adjust the PTZ preset position, right mouse click to back to the original interface after adjustment;

5, Adjustable hold time, after the adjustment, click "Store" Preset

6, Repeat steps 2, 3, 4 presets, after all the setups, click " ? " To enter

7, Check " Tour start ," PTZ start cruising

Description

● Only one channel is set tour by operation above, if you want to cruise another channel, choose "Copy to All" and operate one-button add.

4.14Record function

4.14.1 Manual Recording

Operation Procedure:

1, Left-click on the shortcut menu bar of "Manual Record" or press 【Video/REC】key to enter its setups interface, as shown below:

2, Mouse to select the required video channel , "☑" means to open ; "□" means closed ;

3, Click "OK " button to exit after setup completion, start recording.

Description

● Need to start all channels record operation, check ☑ " All" or click " All on" button ;

● After a successful manual record, the upper right corner of the channel will be displayed;

● To turn off manual record, click on the " All Off " button.

4.14.2 Timer recording

Operation Procedure:

1, Right- click " System Setup" - > "Record Setup" - > " Video Plan " to open the video setups interface, check the timer box, as shown below :

2, Videos of channel and the week can be selected.

3, Click on the " Period 1" , you can set the time range of time record, you can set four time periods simultaneously . As shown below:

4, Mouse tick ☑ check / uncheck the "Time" , the system will turn on / off time record;

5, Click " Apply" or " OK" button.

Description

● When time record is successfully, the top right corner of the the record channel will display

● through the "copy to " all , all channels is set successfully

4.14.3 Motion Video

Operation Procedure:

1, Right- click " System Setup" - > "Recording Setup" - > " Video Plan " to open the video setups interface, mobile check box , as shown below:

：

2, Videos of the week and channel can be selected;

3, Click " Period 1 " , you can set the time range of time record, you can set four time periods simultaneously. As shown below:

4, Mouse tick ☑ check / uncheck the "Motion" , the system will turn on / off motion recording ;

5, Click " Apply" or " OK" button.

Description

● When motion record is successfully set, the top right corner of the channel will display

● Through the "copy to " all channels are set successfully.

### 4.14.4Alarm record

Operation steps:

- 鼠标右键点击“系统设置”->“录像设置”->“录像计划”，打开录像设置界面，勾选报警复选框，如下图所示：

1. Pls right click”system settings”->“Record setup”->”Record Plan”, pls go to the record setup interface and choose the alarm option. Pls check the picture below:

2. The video channel and weekday can be selected.

3. Click”schedule 1“，users can set up the period of time of recording. Four schedules can be setup synchronously. Pls check the picture below:

4. When choose☑/cancel “alarm”by mouse, system will start/close “alarm record”

5. Pls click“Apply” or “ok”.

Illustration

*The upper right corner of the channel setting “alarm record” will show , when “alarm record” has been successfully completed.

*Users have to choose “Alarm” in “alarm setup” and “motion detection”, and choose”record channel” in “alarm setup” , thus alarm record will work.

*All channels can be set up by clicking "copy to" all.

## 4.15 System Setup

Pls click “system admin” in the menu to log into system interface which includes: General setup, Channel setup, Record setup, Network setup and system Admin. Pls check the picture below:

### 4.15.1 General setup

Operation steps:

Pls right click “system setup” on main menu->“General setup” then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| Auto logout | Choose this function, system will logout automatically at setting time. |  |
| Key buzzer | Choose this function, sound can be set up start/close. | There is key buzzer with remote control and panel control. |
| Language | Setup system language. Support 20 kinds of language such as Chinese/English. |  |
| Standard | Setup video standard of the device, support PAL/NTSC. | Only take effect after reboot. |
| Keypad Type | Can choose Type 1,type 2, type3 and type 4. |  |
| Remote ID | Setup remote control code.Default 255. | When using a remote control to operate the device, they are connected by remote ID. Remote operation will only work when they are matched. |
| Boot Wizard | Choose this function, it will show setting guidance interface when device starts up every time,which can help users to set up the basic parameters. |  |
| Show Cloud ID When Preview | Cloud ID of the device will show on the main system interface when choosing this function. | "Position": the position on main interface of cloud ID can be setup. |
| Show Time ID When Preview | Time will show on the main system interface when choosing this function. |  |

Illustration

* It will show setting guidance interface when device starts up every time if choosing ”Boot Wizard” , Pls cancel it if users do not need this function.

#### 4.15.1.2 Time setup

Operation steps:

Pls right click the main menu”System setup”->“General setup”->”Time setup”, then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| Time Zone | Setup world time zone |  |
| Date format | Setup date format : year / month / day, month / day / year, or day / month / year is optional. |  |
| System Date | Set up the current date of the device |  |
| System Time | Set up the current time of the device | "Position": the position on main interface of time can be setup. |
| Sync Time | Synchronize network time and camera time |  |
| Time format | Set up time format of the device. | 12 hours or 24 hours format is optional. |

#### 4.15.1.3 HDD Setup

Operation steps:

Pls right click the main menu”System Setup”->“General setup”->“HDD set up”， then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| Overwrite | It is used to delete recordings automatically when the hard disk is full. |  |
| Format | It is used for HDD Format |  |
| Auto delete old files | It is used to set up the time to delete old file automatically. |  |

Illustration

* The newly installed hard disk can only work normally when formatted on the device.

#### 4.15.1.4 Screen setup

Operation steps:

Pls right click the main menu”System Setup”→“General setup”→”Screen setup”, then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| OSD Alpha | This is menu transparency.User can adjust it according to their preference. |  |
| VGA resolution | It is used to set up the resolution of the monitor, support 1280×1024/1024×768/1366×768/1440×900/1080P@50HZ/1080P@60HZ | Only take effect after reboot. |
| CVBS Output | When errors occur on adjusting the position of monitor , it can be adjusted by up and down, left and right. |  |
| Auto Switch | Setup the time when preview images switch automatically. One-image or four-images is optional. |  |
| Skip Loss | During automatic cruise, it will skip channels with no image. |  |

Illustration

* CVBS Function: when there is offset error of CVBS output, users can use this function to move the image to right position.

* Auto Switch: after starting this function and setting the time, the images on main menu will switch automatically according to the time. One-image or four-images is optional.

* If choosing “Skip Loss” on “Auto switch” , then channel image cruise will skip channels with no image.

### 4.15.2 Channel setup

#### 4.15.2.1 Encode setup

Operation steps:

Pls right click the main menu”System setup”->“Channel setup”->“Encode setup”, then get setting interface as below:

Detailed functions:

| Function Type | Description |
| --- | --- |
| Channel | It is used to show all the channel number of the device |
| Encode mode | It used to set up the encode mode of the device, including video only and audio/video mixed. |
| Main stream | For the stream of the local video |
| Sub stream | For the stream of network transfer |
| Bitrate mode | It is used to change the stream mode, support fixed/variable/average stream |
| Encode format | It is used to change encode format, support 1080P/H-1080P/720P/960H/WCIF/D1/CIF/QCIF/HD1 |
| Limited rate | It is used to show the video file size. Larger value, more clear the video file. But occupied HDD space/network resources is larger. |
| Quality | It is used to adjust image quality, support the highest/high/medium, etc. |
| Frame Rate | It is used for adjusting video fluency. Larger value, smoother video playback, but occupied HDD space/network resources is larger. |

Illustration

* This setting is only for one channel. Users can use "copy to" all if they want to setup all channels.

* Sub stream is used for network transmission. Encoding format, maximum bitrate and frame rate can be less than or equal to main stream.

* "Encode mode" selection determines video playback, video backup and recording with audio output or not. Only select "Audio/Video Mixed" , “video recording”, “video playback” and “video backup” and there is audio output.

- Stream Control Settings:

1、"fixed stream" indicates that the system encodes image according to user-defined bit rate and frame rate;

2 "VBR" means the system encodes image based on user-defined image quality and video frame rate, but the bit rate is adjusted automatically according to the video scene.

3, "Average stream" indicates that the system controls the fluctuation range according to user-defined code rate.

#### 4.15.2.2 PTZ setup

Operation steps:

1. Pls right click the main menu“System Setup”->”Channel setup”->“PTZ setup” then get setting interface as below:

2, When page setup is completed, click "OK" button, the setting information is saved and exit; click "Cancel" button, the setting information is not saved and exit.

Detailed functions:

| Function Type | Description |
| --- | --- |
| Channel | It is used for display all of the channel number |
| Protocol | Optional RS485 and UTC, selected item must be consistent with the matched PTZ protocol. |
| Baud rate | Select the baud rate matched with the connected PTZ |
| Device ID | Enter the specified decoder ID |
| RS485 | Optional pelco-D, pelco-E, selected item must be consistent with the matched PTZ protocol |

Illustration

* On the right of "Copy to" button, select the target channel, click "Copy to", the system will copy the current setting to other target video channel.

#### 4.15.2.3 Channel OSD

Operation steps:

- Pls right click the main menu“System Setup”->”Channel setup”->“Channel OSD” then get setting interface as below:

2.Select the channel, change the channel name

3.Select the color adjustment, adjust the selected channel color

#### 4.15.2.4 Bitrate

Operation steps:

#### 1. Pls right click the main menu“System Setup”→”Channel setup”→“Bitrate

” then get setting interface as below:

Illustration

* Users can view the code stream value of every channel of connected cameras.

### 4.15.3 Record setup

#### 4.15.3.1 Record plan

Operation steps:

#### 1. Pls right click the main menu“System Setup”->”Record setup”->“Record plan

” then get setting interface as below:

Illustration

* "Record setup" can setup time recording, motion recording, alarm recording.

* From schedule 1 to 4, users can setup time(red), motion detection(green), alarm(yellow) to their choice. "☑" means enabled; "□" means invalid. The time bar as below shows the overall schedule from 0-24 hours.

#### 4.15.3.2 Video Detection

Operation steps:

#### Pls right click the main menu“System Setup”->”Channel setup”->“Video detection

” then get setting interface as below:

Detailed functions:

| Function Type | Description |
| --- | --- |
| Channel | Show the channels needed to setup. |
| Sensitivity | Select the sensitivity of motion detection. If choosing "No Detection" , the the parameters in this page are invalid. |
| Detection Type | Set alarm type, including motion, video loss and shield. |
| Alarm duration | To setup the alarm duration when alarm is triggered. |
| Area Edit | Set the detection area. Left click “Area Edit”, then left press the mouse tight and drag the area. |
| Alarm | “☑ means start alarm, “□”means no alarm |
| Buzzer | “☑”Means start Buzzer, “□”means no Buzzer |
| Email Notice | Means start sending E-mail, “□”mean not sending E-mail |
| FTP Upload | “☑”Means start FTP upload, “□”means no FTP upload |
| APP alarm | “☑”Means start mobile APP alarm, “□”means no mobile APP alarm, but support motion detection |

4.15.3.2.1 Alarm setup in video detection

Operation steps:

#### 1. Pls right click the main menu“System Setup”->”Channel setup”->“Video detection

” then get setting interface

2. Select " Detection" ->choose “Motion”to start this function, as picture shown below:

3. Choose “☑Mobile APP Alarm”,click “apply”.

Illustration

* When setting of motion detection is completed, please enter into "Alarm Setup", select the channel and click "Operating Mode", select open usually, and choose ☑ alarm, then motion alarm can come to effect.

* If users only need to detect a narrow area, pls click "Area Edit" and choose the area. Default: selection means start detection, no selection means no detection.

* If users need buzzer, pls pick it.Note: When checked, please enter into "Alarm Setup", select the channel and click "Operating Mode", select open usually, and choose ☑ buzzer.

- * If users need to receive E-Mail notification, pls pick “E-Mail notice”, and then go to “n

* If users need to upload “motion recording, time recording, and alarm recording”to FTP server, pls go to “network setup”->”FTP”,pick it.

* If users need mobile APP alarm,pick it. About mobile APP setup, pls refer to 7.2 login.

#### 4.15.3.2.2 Video loss alarm setup

Operation steps:1. Pls right click the main menu“System Setup”->”Channel setup”->“Video detection

” then get setting interface

- Select " Detection" ->choose “Video loss”to start this function, as picture shown below:

3. Choose ☑Alarm”click Apply..

Illustration

* When setting of motion detection is completed, please enter into "Alarm Setup", select the channel and click "Operating Mode", select open usually, and choose ☑ alarm, then motion alarm can come to effect.

* If users need buzzer, pls pick it.Note: When checked, please enter into "Alarm Setup", select the channel and click "Operating Mode", select open usually, and choose ☑ buzzer.

* If users need to receive E-Mail notification, pls pick “E-Mail notice”, and then go to “network setup”-> "E-Mail" and fill in required information.

#### 4.15.3.3 Alarm Setup

Operation steps:

#### Pls right click the main menu“System Setup”→”Record setup”→“Alarm setup”, then get setting interface as below:

Detailed functions:

| Function Type | Description |
| --- | --- |
| Channel | Show all channels. |
| Work mode | Start alarm or not. |
| Alarm duration | To set up Alarm duration time. |
| Record channel | Setup recording channels when alarm is triggered. |
| Alarm | “☑”Means start alarm, “□”means no alarm. |
| Buzzer | “☑”Means start Buzzer, “□”means no Buzzer. |
| E-mail notice | “☑”Means start sending E-mail, “□”means not sending E-mail. |

Illustration

* On the right of "Copy to" button, select the target channel, click "Copy to", the system will copy the current setting to other target video channel.When the setting is completed, click "OK", the setting will be saved and then exit. Click "cancel",the setting information is not saved and exit.

* There are three types of alarm alert: alarm, buzzer and E-Mail, select the corresponding mode and it will work.

* If users want to receive E-Mail notification, except checking the E-Mail notification, they need to setup some e-mail address information. Pls go to “Network Setup”-> "E-Mail" .

### 4.15.4 Network Setup

#### 4.15.4.1 Network setup

Operation steps:

#### Pls right click the main menu“System Setup”->“Network setup”,then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| IP | For displaying IP address of the device. If users want to change IP address, they can manually enter the IP address. | The default IP address is 192.168.1.114 |
| Subnet Mask | For dispalying the subnet mask of the device. |  |
| Gateway | For displaying the device's gateway address. |  |
| MACl Address | For displaying the hardware address information of the device. |  |
| “Automatically obtain IP” | If choosing this function, users get IP address of the device automatically, otherwise it is set manually. | If choosing this function, users can’t change IP address. |
| Web Port | For setting web port, which is used for data transmission when remote monitoring. When this port is disabled or occupied, users have to change this value. |  |
| E-seenet IP | To show E-seenet IP of the device. | Failure to connect the network will show “off-line”. |
| E-seenet status | It is used for show E-seenet status, online/offline |  |

Illustration

*“E-seenet IP”:This IP is used for setting remote monitoring and relevant parameters.

The web port default to 80.When this port is disabled or occupied, users have to change this value.

#### 4.15.4.2 DDNS

Operation steps:

#### 1.Pls right click the main menu“System Setup”->“Network setup” ->“DDNS”,then get setting interface as below:

2.“☑” Means start DDNS service, “□” means no DDNS service. Select the corresponding service providers, and enter user name, password, and domain name.

Detailed functions:

| Function Type | Description |  |
| --- | --- | --- |
| Provider | Provider of dynamic domain name server |  |
| Domain name | Users need to apply for a domain name with the provider |  |
| User name | Registered name of the device on the server. |  |
| Password | Registered password of the device on the server. |  |

3. Click”Apply”, then finish setting.

Illustration

* About automatic analysis of dynamic domain name, now support Dyndns.

#### 4.15.4.3 FTP

Operation steps:

#### 1.Pls right click the main menu“System ”->“Network setup” ->“FTP”,then get setting interface as below:

2.Enable FTP function.

3.Fill in FTP server, port, user name and password and other information.

4.Setup time, click the "Test" button, and then click the "Apply" if test succeeds.

Illustration

* It is used to upload alarm or motion detection results.

#### 4.15.4.4 PPPoE

Operation steps:

#### 1.Pls right click the main menu“System Setup”->“Network setup” ->“PPPoE”, then get setting interface as below:

2.“☑ PPPOE”means connect network by PPPoE(Point-to-Point Protocol over Ethernet)， “□”means not start this function.

PPPOE user: enter the user name provided by ISP.

PPPOE password: enter the password provided by ISP.

* When the setting is completed, click "OK", the setting will be saved and then exit. Click "cancel",the setting information is not saved and exit.

Illustration

* PPPOE user name, password are available from service provider. If setup is completed, reboot the device and dial-up automatically. after dial-up successfully, the network information can be displayed in the network state.

#### 4.15.4.5 3G

Operation steps:

#### 1. Pls right click the main menu“System Setup”->“Network setup” ->“3G”,then get setting interface as below:

2.“☑ open” means start 3G function, “□”means not start it.

3.Select Service Provider: user-defined/China Telecom/China Mobile/China Unicom/ India/AIRTEL/India BSNL/India MTNL/India MTS and so on.

4.Enter dial number, APN, PIN, user name and password. The system will be show up prompt interface if dial-up successfully.

Detailed functions:

| Function Type | Description |
| --- | --- |
| Service Provider | user-defined/China Telecom/China Mobile/China Unicom/ India/AIRTEL/India BSNL/India MTNL/India MTS and so on. |
| Dial Number | Provide 3G mobile phone number. |
| APN | Access Point Name. different operators have different access points. |
| PIN | Equivalent to the phone card password. The original set by provider is 1234 or 0000. |
| User name | Mobile user name |
| Password | Mobile password |

Illustration

* If setup succeeds, the device will dial-up automatically after reboot or power off.

#### 4.15.4.6 E-Mail

Operation steps:

#### 1.Pls right click the main menu“System Setup”->“Network setup” ->“E-mail”, then get setting interface as below:

Detailed functions:

| Function Type | Description | Remark |
| --- | --- | --- |
| SMTP server | Select or enter SMTP server. | SMTP server of email address, E.G. Hotmail: smtp.live.com |
| Port | Setup port number of mail server | default 25 |
| User name | For setting the sender's email address user name | Full email address: like 123456@hotmail.com |
| Password | For setting the sender's email address password | Email address password |
| Encryption type | Choose safety type of email service | None means unsuccessful. Then pls choose SSL |
| Sender | Email address of the sender |  |
| Sendee1 | Email address of the sendee1 |  |
| Sendee2 | Email address of the sendee2 |  |
| Subject | Email subject. default “DVR Report” |  |
| Interval | Set up the interval of sending email |  |
| Health mail interval | For checking the health status of the device. |  |

2“☑ Open”means enable E-mail function, “□”means not enable.

Illustration

* Start "health mail interval", system will detect whether the device crashes or not automatically. Emails are sent every 30 minutes.

### 4.15.5 System Admin

#### 4.15.5.1 System version

Operation steps:

#### Pls right click the main menu“System Setup”->“System admin” ->“System version”then get setting interface as below. Users can see the device name, device model, serial number, hardware version, software version, and other related information.

Illustration

* When users need to upgrade the software, pls check the device model and software version and then get corresponding upgrade firmware .

* The serial number of each device is unique. The last 9 numbers is device ID.

#### 4.15.5.2 HDD info

Operation steps:

Pls right click the main menu“System Setup”->“System admin” ->“HDD info”, then get setting interface as below. Users can check the hard disk type,capacity,used status.

#### 4.15.5.3 System log

Operation steps:

1.Pls right click the main menu“System setup”->“System admin” ->“System log”, then get setting interface as below:

2.Choose event type, check time period, click "Search", then show up corresponding log information. Users can go through the information by clicking the "up page" / "next page" or enter the target page.

Illustration

* The content  of "Log information" is stored in the hard disk. Users can’t see it without a HD.

* The content of "Log information" can’t be derived. Users can only check the info on the software.

#### 4.15.5.4

#### 4.15.5.4 User

Operation steps:

Pls right click the main menu“System setup”->“System admin” ->“User”, then get setting interface as below:

2.When the setting is completed, click "OK", the setting will be saved and then exit. Click "cancel",the setting information is not saved and exit.

Detailed functions:

| Function Type | Description |
| --- | --- |
| Add user | Input a new user name and password in the edited column, setup operation access, choose in the corresponding functions,“☑”means user have the access, “□”means have no access. |
| Delete user | To delete the chosen user. |
| Edit user | Revise the access of chosen user. |
| Set password | change password of current registered user, add old password and new password and click “OK”. |

Illustration

* Delete user: anyone except Admin can’t setup or delete other users.

* Edit user: anyone except Admin can’t setup the access of other users.

* When adding a new user, the user name only can be capital and lowercase letters and numbers.

* When adding a new user, if choosing as VIP user, defaults to be access to all functions.if choosing as a common user, then have setup access. “√”means users have access, “□”means users have no access.

#### 4.15.5.5 System maintenance

Operation Steps

Way one:

1. Pls right click the main menu“System setup”->“System admin” ->“System maintenance”, then get setting interface as below:

2.Enable “Auto maintenance”.

3.Select the time of auto maintenance.

4.System will be auto reboot when the setting time is up.

Way two:

1.Right click main menu, select “one key to surf Internet”, check if network is working or not. If not, please setup the network configuration according to previous instructions.

2.Right click main menu, “System setup”->“System Admin”->“System maintenance”, get operation interface.

3.Choose “Online upgrade”, select “Upgrade when finish download”, click “Start”.

4.When there is new version, system will download the firmware to upgrade automatically. The upgrade progress can be checked from progress bar. Once system is upgraded completely, device will reboot.

#### 4.15.5.6 Software update

Steps

1.Pls right click the main menu“System setup”->“System admin” ->“System upgrade”, then get setting interface as below:

2.Copy firmware under USB disc root folder, insert USB disc to USB port.

3.Click USB storage-system-start

4.The progress of upgrading can be checked from the progress bar, once system upgrades completely, device will reboot.

Illustration

* Make sure the upgrade firmware is in the root directory of USB disk before upgrading.

* Types of upgrade: system,start-up logo and resources.

* Don’t cut off power during upgrading, or device will be unable to reboot.

* Make sure device connects network successfully before online upgrade.

* The server address, port, network route can be defined during online upgrade.

#### 4.15.5.6 Factory setting

Operation Steps:

1. Pls right click the main menu“System setup”->“System admin” ->“Factory setting”, then get setting interface as below:

2.In Admin interface, choose “factory reset”and enter setting interface.

3. Select the item required for factory reset, click “OK”to save setting info and exit;click “cancel”,the setting information is not saved and exit.

Illustration

* After factory setting, all setting will get back to original status. Pls use this function with great caution.

# Chapter 5  LAN access

## 5.1 Log in

Steps as follows:

1.Open the internet browser

2.Input NVR’s IP address:http://IP*** on the browser, eg.input http://192.1.1.28 , and enter “login”page, see the picture below:

3. Input the correct user name and password.

4.Click “log in” to the preview page, see the picture below:

## 5. For the first login, download and run the WebClient.exe widget.

6. Log in again, and users can get preview, see the picture below:

Illustration

IP address can be checked from network setting in system setting

Support multiple users log in different PC.

If the web port No.is revised (default 80),when input IP address on browser, port No. is needed to input after IP address.eg.192.168.1.28:102

If software is unable to load at the first time of use, below setting is required on browser:

“tools”- “Internet options”- “security”- “user-defined level”- start both Active X widget and Plug-In, then click “OK”.

## 5.2   Preview

Enter to preview page after log in successfully, showed as below:

Illustration

- Support 1CH,4CH,9CH,16CH pictures.

- Support main stream and sub stream selection

## 5.3 Playback

Operation Steps:

- Click playback sign in preview page.

- Enter to playback page, showed as below :

- Setup checking time, type and channel, click “Search”.

- Select the channel to check playback data.

Illustration

- Make sure the user have access to playback when common user log in. The playback authority can be checked and given in system setup - system admin - user - edit user.

## 5.4

## 5.4  Configuration

Operation steps:

- Click configuration sign  in preview page.

- Enter to configuration page, showed as below:

Illustration

- Refer to system functions introduction for the detailed configurations.

- Make sure the user have access to remote configuration when common user log in. The remote configuration authority can be checked and given in system setup - system admin - user - edit user.

# Chapter 6: Eseenet Access

## 6.1 Esee ID login

Operation Steps:

- Open the browser

2、Enter http://www.dvr163.com , showed as below:

3、Enter correct device ID and password.

4、Log in to preview page, showed as below:

Illustration

Device ID can be obtained from system setup - network setting, select eseenet (P2P), or click “one key to surf the Internet”, then the current device ID can be checked.

Only when the esee ID is online then users can remotely log in.

## 6.2 Username login

Steps

- Open browser

- Enter http://www.dvr163.com , select “user name log in”,showed as below :

- Register an user when first login.

## 6.3 Playback

Operation Steps:

1、

Click playback sign on the preview page, enter to search page, click search, showed as below:

Double click the files, the playback video will display on the right interface.

# Chapter 7: Mobile APP

## 7.1 Introduction

Support mobile remote access.After device is connected to network, users can enter the device’s cloud ID No. or  LAN IP address or dynamic DNS at adding device column on mobile APP, and get mobile remote monitoring.

Illustration

Currently, mobile APP support Chinese, English, German, French, Russian, Dutch, Italian, Spanish, Turkish and other languages, the language on APP is the same as that on mobile phone system.

There are two access way in App: Eseenet and Lan access

Support android and ios

Apply dynamic DNS to providers, fill in the info at DDNS Dynamic Columns on “network setup” of the recorder

## 7.2 Log in

Steps

### 7.2.1、Installation

Way one: Download and install from major Android APP markets, eg. Google play, go to Google play to search IP Pro, install after complete download.

Way two: Use mobile phone to scan directly the QR code in the boot wizard of device, go to the download page and download and install it on the mobile phone.

### 7.2.2、 Open software

showed as below

Illustration

When the first installation is completed, device will open a login page, if you do not have a login account, register an account to login, after success login, every time when opening software, it will go directly into the device interface. Fill in an user name and password information when registering, enter the mailbox (to retrieve the password when password is forgotten, you can also skip it), you can also choose to experience adding a device on software.

If choose to experience,  login page will be first entered every time of opening the software

Account information will be stored on the server after login, when login the account in another mobile, the previous added device will be displayed automatically, no need to add again. If just to experience, the added device information can not be displayed in another phone.

### 7.2.3、 Adding device

Click the sign “+” on the right upper side, choose cloud ID, fill in recorder’s connection info, as below showed:

Notice

| IP PRO ID | The facility ID of IP PRO. |
| --- | --- |
| Descriptions | Descriptions of device (eg. Device model no.) |
| User name | User name of added device |
| Password | Password of added device |
| Channel | In the experience mode, users need to select the number of channels according to the added equipment. In user mode, the server will automatically detect the number of channels in device, no need user to select. |
| Submit | Click “Submit” to add device |
|  | Click to cancel and return back to “My device” page |

Click “+” to add an device, cloud ID, ip / DDNS, LAN scanning is optional

System will automatically recognizes the ID’s number of channels, click “submit” to add after the success add.

Select the correct channels under experience model, the default channels is 4CH.

### 7.2.4、  Preview

Click the added device into preview page. The default channel is 4CH, choose a channel for preview. As shown below:

Notice

- Support max 16CH preview in the same time

Support 4/6/8/9/13/16 ch split screen preview in the same time

### 7.2.5、  Remote playback

Click remote playback in preview page to the playback page, as shown below:

Notice

Remote playback can pull the bars to select a specific certain period of time, select a specific channel to playback.

- Support 1ch playback

- When there is voice in record, playback will also has voice.

When select the record,  record can be the same time during playback, record will be saved in the phone.

Select the capture to catch the current playback image.

### 7.2.6、  capture / record / quality

Notice

- Select capture to catch the current image

- Select record to save video in mobile

Select quality to choose HD or SD, HD is main stream, SD is sub stream

### 7.2.7、   Mobile APP Alarm

Click “Me” to enter into operation interface, choose “ Alarm setting” to open alarm information. Setup the APP alarm notice on mobile, go to alarm information column to check alarm details.

Notice

- Login with available account, different account login is unable to setup alarm.

Before adding device, make sure to setup mobile APP alarm on the testing type column of device, refer details on 4.15.3.2.1 motion testing alarm settings , or the alarm information still can’t be sent to mobile even alarm is on.

# Chapter 8: Appendix

## 8.1 Hard disk capacity unit conversion

| Device capacity unit conversion | Operation capacity unit conversion |
| --- | --- |
| B | 1 B ＝ 8 b | B | 1 B ＝ 8 b |
| MB | 1 MB ＝ 1000 KB | MB | 1 MB ＝ 1024 KB |
| GB | 1 GB ＝ 1000 MB | GB | 1 GB ＝ 1024 MB |
| TB | 1 TB ＝ 1000 GB | TB | 1 TB ＝ 1024 GB |

Notice

- 1GB＝1000MB。

Device capacity unit conversion mode is same as hard disk supplier, all takes 1GB＝1000MB.

## 8.2 Record required capacity caculation.

- A＝B÷8÷1000×3600

Single images video file size per hour

- A＝B÷8÷1000×3600×24×N

N-channel images video file size per day (24 hours)

- A＝B÷8÷1000×3600×24×D×N

N-CH video image file size in D-day

Notice

A is the required hard disk capacity, B is the bit rate size, N is the channels of record, D is the days of recording.